## Slide 1: E224 – 2014 Results

## Slide 2: Experimental Goals for 2014
Demonstrate the feasibility of detecting phase modulation of a probe pulse by a plasma at a single image plane in a low density (<1E17) plasma.

## Slide 3: Results from 2014
Observation of plasma modulated probe pulse:
  From laser ionized plasma
  From beam ionized plasma
Development of an in-oven alignment technique
Observation of laser-heated plasma
Observation of plasma structure evolution over ps-ns-us time scale.

## Slide 4: Probe Pulse Modulation
No Plasma
Laser-Ionized Plasma
Beam-Ionized Plasma
Observation of “bow-tie” pattern modulation of probe pulse by laser and e-beam ionized plasma.

## Slide 5: “In-Oven” Alignment
We can simultaneously image the axicon focus and the location of the beam ionized plasma at a single z location. This image provides a new technique for aligning the axicon focus to the e-beam.
e-beam
axicon
Before Alignment
After Alignment

## Slide 6: Laser-Heated Plasma
¼ Power
½ Power
Full Power
The diffraction pattern observed in the probe pulse becomes chaotic at high laser power. We used this diagnostic to optimize our laser power so that we are ionizing, but not heating the plasma.

## Slide 7: Timing Studies
100 ps Delay
1 ns Delay
We varied the timing of the probe pulse with respect to electron beam arrival time and observed the expansion of the beam-ionized plasma channel.

## Slide 8: Simulation Work
Instead of simulating the whole large probe, the diffraction of a thin laser beam through the plasma is calculated with the Fresnel formula (near-fear diffraction), and integrated at multiple z locations.
The whole probe is recovered with a waterfall plot in z.
Z = +1
Z = 0
Z = -1
α
Plasma plane = diffracting object
We are preforming optics calculations to model our system and compare observations with expected results for different plasma shapes.
Light from the probe, seen as a sum of multiple fine ray
Image plane

## Slide 9: Simulation Work
On the left : Probe pulse diffraction observed from a beam-ionized plasma column.
Below : Simulation of Fresnel diffraction from a uniform cylinder of plasma. α = 1/100 rad
Plasma radius = 100E-6 m
Plasma radius = 200E-6 m

## Slide 10: Experimental Setup for 2014 Diagrams and Images

## Slide 11
Pickoff System
P1
Axicon
P2
Waveplate
P3
Pickoff System

## Slide 12
Output System
DS Gold Mirror
Motorized beam splitter
1m lens
DS_GOLD GigE
E224_Align GigE

## Slide 13
Output System
Alignment screen
Spatial Filter
E224_Probe GigE with 800 nm interference filter
Image Plane

## Slide 14
IP Box
6” Cube
E224 Simple Diagram
Image Point
λ/2
Compressed Laser Pulse
Plasma Volume
CCD
Axicon
Polarizer
1 m Lens
Ionization Pulse
Probe Pulse